## Slide 1: WaLLe: Final Project AAMR
Sahil Arora
32953

## Slide 2: Rough work
General intro in 2 lines
360 rotation
most profitable target
if stuck then see where is space and move there
retry for 4 times
at end of program go home

## Slide 3: How is Everything Working ?
Uses a Navigation Stack with /move_base, /amcl, /map_server nodes.
Target points are published to /goal_publisher.
WallE uses /amcl_pose to get position and orientation.
Targets are sequentially published to move_base_action_client:
  It computes Global and Local Path.
  Publishes to velocity commands to /cmd_vel.
  Local mapping checks for real-time obstacle range with provided sensors.

## Slide 4: 360° Rotation on start-up
WallE need to fully know its current positions before it starts for a target.
Calls a function to rotate 360° degree in 10 seconds --> Converged particle cloud.
Why: If this is not done it poses problem when robot is spawned very near to a goal point.

## Slide 5: Where to go first?
Simple heuristics to maximize reward while being lazy.
Greedy: Searches through whole target set.
Not that smart: In cases, it ends up travelling more.
Most Profit:
  , considering Eucledian-Distance

## Slide 6: If I am stuck due to Planning inconsistency ?
Robot stucks when Planner estimtes cost as negative.
Need an algorithm to go back to free space.
Max space: Identifies the region with max space and re-orients/ re-position.

## Slide 7: What if I am unable to reach the target ?
Keeps a time window of 10 seconds and checks displacement after the time interval.
  if displacement < threshold, then append goal to later_goal
It may be because another robot was standing at goal.
Or due to inability of path planning.
After all points from all_target list are tried then goals from later_goal are retried at max 4 times.

## Slide 8: Go home if tired !
After retry algorithm, Walle doesn‘t intend to block path for others.
It drives to origin(0,0) and asks: